## Slide 1: Overview of Process Lines
Automated side arm Console; orthopedic implants
Automated side arm E-Coat Line; mintage
Automated side arm Phosphate Line; automotive
Automated ½-ton Zinc + Chromates; job shop
Automated 2-ton pantograph Pickle Line; titanium
Manual 7½-ton gantry Pickle Line; steel wire
Automated 7½-ton gantry Pickle Line; steel wire
Automated 10-ton crane Chemical Etch Line; titanium

## Slide 2: Automated side arm Console; orthopedic implants

## Slide 3: Automated side arm E-Coat Line; mintage

## Slide 4: Automated side arm Phosphate Line; automotive

## Slide 5: Automated ½-ton Zinc + Chromates; job shop

## Slide 6: Automated 2-ton titanium pickle Y-config.

## Slide 7: Manual 7½-ton gantry Pickle Line; steel wire

## Slide 8: Automated 7½-gantry Pickle Line; steel wire

## Slide 9: Automated 10-ton crane Chemical Etch Line; titanium

## Slide 10: Process Line Morphology:
Tank lines versus Consoles
Enclosures versus Ventilation systems
Polypropylene versus stainless /carbon steel lined
Homo polymer versus European Grey co-polymer
Containment: berm /pan versus pit
Scrubber: at grade versus roof
Wastewater Treatment: at grade versus mezzanine
Circulation around the line: minimum of 4ft clear
Notes: Chemical compatibility - longevity – elasticity - repairability -

## Slide 11: Material Handling
Gantry: structure, rail type, lifting (wire, chain, belt)
Side arm: cost, moment load, belts, chains, slides
Rimrunner: continuous pinch point, blocked access
T-stroke versus J-stroke
Number of pickup/drop-off points
Positioning Systems: open-loop versus closed-loop
relative absolute
rotary, bar code, infrared, laser
Safety interlocks and e-cord

## Slide 12: Fume extraction, Plenums, Ducts, Scrubber, Make-up and Push-Air
Process tanks: surface area, chemistry, temps
Heated rinses: is direct discharge cost effective
Air flow at tanks 2 to 3 fps = ft³/minute for sizing
Side plenum slot velocity 10 to 16 fps (adjustable)
Rear duct velocity 36 to 48 fps to prevent dropout
Make-up air: 90%-95% of extraction; laminar flow
Push-air: only affect front of tanks for operators
Eductors versus air-agitation
Notes: 2 or 3 based on chemistry and temperature

## Slide 13: Water optimization
Cascades: 2 or more stages, with halo sprays
Fills: intermittent versus feed rates;rotometers
Rinse reuse within line or for neutralization
recycle and reuse
Notes: 10:1 dilution factor – JM in WA 5x best is solenoid-to-rotometer reuse

## Slide 14: Controls
PLC versus PC, hybrid systems (60bpm heartbeat)
PC high level
PLC low level and safety (limitations)
Reservation system versus random loading
ISO and Nadcap documentation and certification
Notes: cortex/brain stem ±20 barcodes v 14,000